## Slide 1: PX4 Hawk Position Estimator

## Slide 2: Multirotor Flight Control

## Slide 3: Position_estimator_inav
Position estimator inav app is position estimator, based on inertial model, optimized for multirotors. It reads multiple sensors and estimate 3D position and velocity, in local and global frames. It can be used with position control apps, e.g. multirotor_pos_control.

## Slide 4: Basic structure
int position_estimator_inav_main(int argc, char *argv[])
  start
  stop
  status
int position_estimator_inav_thread_main(int argc, char *argv[]) // thread 로 동작

## Slide 5: Data Source
The following sources (with corresponding parameters for weight) are available for altitude
Accelerometer- acceleration (W_ALT_ACC)
Barometer- Absolute altitude (W_ALT_BARO)
Sonar- relative altitude (W_ALT_SONAR)
The following sources (with corresponding parameters for weight) are available for position
Accelerometer (W_POS_ACC)
GPS Position (W_POS_GPS_P)
GPS Velocity (W_POS_GPS_V)
Optical Flow (W_POS_FLOW) NOT IMPLEMENTED YET

## Slide 6: Data Output
Local Position
  X,Y,Z
  Velocity of X,Y and Z
  Eph //error horizontal
  Epv //error vertical
Global Position (Earth Coordination)
  Latitude
  Longitude
  Altitude
  Velocity of NED
  Eph
  Epv